## Slide 1
CN-002 Real Data Application
July 2016

## Slide 2: 主要内容
Real Data Application (RDA)概述
创建脚本（Provisioning）
运行脚本
日志实时查看和分析
支持和帮助
附录

## Slide 3: Real Data Application (RDA)概述
TM500 & RDA集成测试环境
RDA产品架构及简介
RDA环境连线
RDA客户端

## Slide 4: RDA业务服务器
常提及的几个名称
  diversifEye是业务服务器产品的统称，包含D500/D1000/R630。diversifEye集成到TM500测试环境后，在软件层面，又被称为Real Data Application (RDA).
  diversifEye是业务服务器客户端，最新的客户端已更名为TeraVM.
  Shenick是业务服务器的提供商，以前是Aeroflex的合作伙伴。
  Shenick后来被Aeroflex收购；Cobham后续又收购了Aeroflex.
功能
  多小区测试环境下，为成千上万终端并行提供各种数据业务。
  模拟的应用程序包括FTP/HTTP/TeraFlow/RTSP/VoLTE/PING等等。
  同时模拟应用程序客户端（Edge）和服务器（Core）。
  支持端到端的测试，实时QoS以及应用程序级别的关键性能指标评估。
  D500/D1000最多并行支持6个TM500测试环境。

## Slide 5: TM500 & RDA集成测试环境
#待补充真实测试环境图示

## Slide 6: TM500 & RDA集成测试环境
Hosts and traffic applications are configured on a single GUI
Edge side
Core side

## Slide 7: RDA产品架构
  Traffic Generation Options
  3.6Gbps DL Traffic – R630
Application Options
Voice services
Video services
Passive Analysis
TWAMP
SMS over IMS
Thresholding
TeraFlow
Ping
HTTP
eMail
FTP
Hardware Platforms
D500
D1000
R630
  2.7Gbps DL Traffic – R630
  1.8Gbps DL Traffic – R630 or D1000 Edge+Core
  900Mbps DL Traffic – D500 Edge+Core
  450Mbps DL Traffic – D500 Edge

## Slide 8: RDA平台简介
D500 – D1000 – R630
D500
I/O – 1x 1Gbps
Fixed VLANs per User
  SGi Servers I/O use VLAN tags
Number of UEs
  6 000
Number of Applications
  24 000 provisioned application clients
  12 000 concurrent application clients
Number of PDN connections
  12 000
Number of fine statistics
  500 entities
D1000
I/O – 2x 1Gbps
Fixed VLANs per User
    SGi Servers I/O use VLAN tags
Number of UEs
    12 000
Number of Applications
    48 000 provisioned application clients
    24 000 concurrent application clients
Number of PDN connections
    24 000
Number of fine statistics
    500 entities
R630
I/O – 2x 10Gbps
Configurable VLANs per User
  SGi Servers can be used without VLAN tags
Number of UEs
  36 000
Number of Applications
  288 000 provisioned and concurrent application clients
Number of PDN connections
  72 000
Number of fine statistics
  24 000 entities
Near-real time Streaming of statistics

## Slide 9: RDA平台简介
D500 – D1000 – R630

## Slide 10: RDA业务关键性能分析
per Application
per flow performance measurements
per UE
Aggregate performance

## Slide 11: RDA环境连线
#待补充环境连线图
Standalone D500 Edge/Core

## Slide 12: RDA环境连线
#待补充环境连线图
D500 Edge and Core Pair

## Slide 13: RDA环境连线
#待补充环境连线图
Standalone Edge/Core D1000

## Slide 14: RDA客户端
早期的RDA客户端diversifEye，最新的客户端TeraVM
默认的管理IP地址：192.168.10.200.
请通过网页浏览器登录管理页面，下载安装RDA客户端。
  默认安装即可
访问某些RDA管理页面需要用户名和密码。
  用户名：diverAdmin
  密码：diversifEye
下载及安装

## Slide 15: RDA客户端
下载及安装

## Slide 16: RDA客户端
通过客户端diversifEye/TeraVM登录RDA
  User Name：tm500（不建议用其它用户名，因为可能导致TM500无法调用RDA脚本）。
  Server Host: 192.168.10.200 （默认）。
  Partition: 根据RDA测试环境连线，选择对应的Partition.
登录

## Slide 17: RDA客户端
基于Java的GUI

## Slide 18: RDA客户端
Test Groups/Applications

## Slide 19: RDA客户端
Nodes

## Slide 20: RDA客户端
Hosts

## Slide 21: RDA客户端
Statistic Groups

## Slide 22: RDA客户端
Thresholds

## Slide 23: 创建脚本（Provisioning）
Python安装和设置
RDA Provisioning
导入和导出脚本

## Slide 24: Python安装和设置
Provisioning ：通过配置文件（tm500.xml），用Python批量生成RDA脚本，这个过程称为Provisioning.
电脑运行环境配置
  依次下载安装Python相关软件
    python-2.7.5.msi
    pywin32-214.win32-py2.7.exe
    wxPython2.8-win32-unicode-2.8.12.1-py27.exe
    xlrd-0.7.9.win32.exe
  添加Python安装路径（ C:\Python27\）至系统的环境变量。
    右键点击“我的电脑”，选择“属性”；
    选择“高级” -> “环境变量”
    注意：Win7和Win10对应的环境变量配置界面略有区别。

## Slide 25: Python安装和设置

## Slide 26: RDA Provisioning
每个CUE TM500软件的安装目录下都有Provisioning模板，例如：
Win7和Win10的C:\Program Files\和C:\Program Files (x86)\目录下的操作需要管理员权限，所以请把Provisioning拷贝到其它路径再进行修改及其它操作。
根据测试需求，有两个文件需要更新
  live.bat
  TM500.xml

## Slide 27: RDA Provisioning
live.bat: 批处理文件，配置基本环境变量，调用shenick.py生成RDA脚本。需要更新以下信息：
  aflx_ip_addr：RDA IP地址
  aflx_group_name：RDA脚本名字
  aflx_part：Partition
live.bat

## Slide 28: RDA Provisioning
TM500.xml: RDA配置文件，live.bat将根据此配置文件生成相应的RDA脚本并自动上传至RDA。
配置文件主要包含以下模块
TM500.xml

## Slide 29: RDA Provisioning
模板默认配置
建议更新如下配置
  Use_Scaled_Entities
  Background_Ping
基本配置信息

## Slide 30: RDA Provisioning
模板默认配置
请根据测试需求及环境更新如下配置
  Total_UEs
  PDNs_per_UE
  LAN_IP：TM500业务口IP地址，用于PPPoE拨号
如果是VoLTE相关测试的话，一般建立两个APN，配置更新如下
TM500 Block

## Slide 31: RDA Provisioning
模板默认配置（IPv4），建议采用默认配置。
模板默认配置（IPv6）
如果是IPv6 VoLTE UE的话，第二个APN用于承载VoLTE，对应的APN为1，配置更新如下所示
  IPv6_PPPoE_Client
PPPoE Block

## Slide 32: RDA Provisioning
Application模块配置包含两部分
  服务器相关配置
  客户端相关配置
    默认配置（<Default>）：默认客户端
    Profile_N配置（<Profile_N>）：除了默认客户端，同一个服务器还可以配置多个客户端。
Application Block

## Slide 33: RDA Provisioning
模板默认配置
主要待更新配置
  Type/Host_Name/IP_Address
FTP Server Configuration

## Slide 34: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Server_Host_Name
FTP Client Configuration (Get)

## Slide 35: RDA Provisioning
默认模板配置
主要待更新配置
  UE/PDN/ Server_Host_Name
FTP Client Configuration (Put)

## Slide 36: RDA Provisioning
默认模板配置
主要待更新配置
  Type/Host_Name/IP_Address
HTTP Server Configuration

## Slide 37: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Server_Host_Name
HTTP Client Configuration (GET)

## Slide 38: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Server_Host_Name/File_Size/POST_Content
HTTP Client Configuration (POST)

## Slide 39: RDA Provisioning
模板默认配置
#待进一步拓展。
HTTP Client Configuration (HEAD)

## Slide 40: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Alias/File_Size
HTTP Client Configuration (IM)

## Slide 41: RDA Provisioning
模板默认配置
主要待更新配置
  Ip_Version/IP_Address
VoLTE Server Configuration

## Slide 42: RDA Provisioning
模板默认配置
VoLTE Client Configuration (Digest)

## Slide 43: RDA Provisioning
主要待更新配置
  Username/Password
  Domain
  SIP_Auth_Username
  Call_Duration
  Media_Type
  Silence_Ratio
  Silence_Length
  Codec
  BHCA
  Pattern
VoLTE Client Configuration (Digest)

## Slide 44: RDA Provisioning
主要待更新配置
  Username/Password
  Domain
  SIP_Auth_Username
  Call_Duration
  Media_Type
  Silence_Ratio
  Silence_Length
  Codec
  BHCA
  Pattern
  VoLTE Section
    AKA_Key
    AKA_Operator_Id
    ESP_Encryption_Algorithm
    ESP_Auth_Algorithm
VoLTE Client Configuration (AKA)

## Slide 45: RDA Provisioning
VoLTE Client Configuration (AKA)

## Slide 46: RDA Provisioning
模板默认配置
主要待更新配置
  Type/Host_Name/IP_Address
RTSP Server Configuration

## Slide 47: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Server_Host_Name/RTSP_Media_Profile/Media_Stream_Duration
RTSP Client Configuration

## Slide 48: RDA Provisioning
cPing不需要配置对应的Server.
模板默认配置
主要待更新配置
  UE/PDN/Ping_IP_Address/Start_After/Stop_After/Delay_Between_Pings/Packet_Size
cPing Client Configuration

## Slide 49: RDA Provisioning
模板默认配置
#待进一步拓展。
sPing Server & Client Configuration

## Slide 50: RDA Provisioning
模板默认配置
主要待更新配置
  Type/Host_Name/IP_Address
TeraFlow Server Configuration (UL UDP)

## Slide 51: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Alias/Server_Host_Name/Start_After/Stop_After/Throughput/Throughput_Metric
TeraFlow Client Configuration (UL UDP)

## Slide 52: RDA Provisioning
模板默认配置
主要待更新配置
  Type/Host_Name/IP_Address
TeraFlow Server Configuration (DL UDP)

## Slide 53: RDA Provisioning
模板默认配置
主要待更新配置
  UE/PDN/Alias/Server_Host_Name/Server_on_PPPoE/Start_After/Stop_After/Throughput/Throughput_Metric
TeraFlow Client Configuration (DL UDP)

## Slide 54: RDA Provisioning
默认模板不含TWAMP相关配置，如有测试需求，请依据如下信息分别配置TWAMP Server/Client.
主要待更新配置
  IP_Address/Delay_Between_Packets/Payload_Size
TWAMP Server & Client Configuration

## Slide 55: RDA Provisioning
模板默认配置
Profile_0 Configuration

## Slide 56: RDA Provisioning
如果不想定义Profile_0，请更新上述配置为</Profile_0>.
Profile_0 Configuration

## Slide 57: RDA Provisioning
模板默认配置
主要待更新配置
  Gateway_IP/Gateway_IPv6
Network Configuration

## Slide 58: RDA Provisioning
live.bat和TM500.xml配置完成后，请在Provisioning文件夹打开DOS窗口，然后运行live.bat即开始生成脚本。

## Slide 59: RDA Provisioning
脚本生成成功后，将在Provisioning文件夹保存一份RDA脚本，同时也将自动导入一份脚本至RDA.
  可以在RDA客户端进一步更新Application/Host对应的配置。更多配置信息，请参阅本文档附录的Applications & Hosts Properties.
如果脚本生成失败的话，请查看DOS窗口打印的信息，以及Provisioning文件夹下的shenick.log，以进一步定位问题。
  如果需要寻求TM500 FAE协助定位，请提供以下信息
    TM500.xml
    shenick.log

## Slide 60: Host Physical Interface
Standalone D500 VLAN Hub端口示意图
Standalone D500 – Edge/Core

## Slide 61: Host Physical Interface
Edge VLAN Hub端口示意图
D500 Pair -> Edge

## Slide 62: Host Physical Interface
Core VLAN Hub端口示意图
D500 Pair -> Core

## Slide 63: Host Physical Interface
D1000

## Slide 64: 导入和导出脚本

## Slide 65: 导入和导出脚本
RDA脚本可以导出保存为.xml格式。
可以通过文本编辑器（例如UltraEdit或Notepad++）编辑RDA脚本，例如批量替换PPPoE IP (<service_name>tm500_lte_10.99.0.2_500_0</service_name>)或者Physical Interface (<physical_interface>11/1/0</physical_interface>)，然后再导入RDA，实现RDA脚本批量快速修改。

## Slide 66: 运行脚本
TM500调用RDA脚本
手动运行脚本

## Slide 67: TM500调用RDA脚本
TM500通过cli命令调用运行RDA脚本.
  运行/终止脚本
  设置PPPoE为In/Out of Service状态
  设置Applications为In/Out of Service状态

## Slide 68: 手动运行RDA脚本
通过RDA客户端运行脚本：选中脚本，然后点击左上角绿色按钮运行脚本。

## Slide 69: 手动运行RDA脚本
手动设置对应UE的Application/PPPoE为In/Out of Service状态
设置Application为In Service状态之前，首先需要确保PPPoE已经处于In Service状态且PPPoE建立成功（已获取UE IP地址信息）。

## Slide 70: 设置Application/Host状态
Set In Service

## Slide 71: 设置Application/Host状态
Set Out Of Service

## Slide 72: 统计日志分析和保存
实时查看统计日志
保存统计日志
实时抓取PDU

## Slide 73: RDA Statistics
RDA Statistics分为两大类
  Normal Statistics：每30秒钟输出一次统计，默认打开；
  Fine Statistics：每1秒钟输出一次统计，默认关闭；
支持实时查看统计信息
  基于图形曲线
  基于列表
测试脚本运行以后，统计相关的日志自动保存在RDA上，可通过如下方式把日志保存到RDA控制电脑上。
  测试脚本正在运行，请用Save Current Detailed Results保存日志。
  测试脚本已经停止运行且还尚未再次运行脚本，请用Save Historical Detailed Results保存日志。

## Slide 74: 实时查看RDA Statistics
Fine Statistics默认关闭

## Slide 75: 实时查看RDA Statistics
Fine Statistics打开

## Slide 76: 实时查看RDA Statistics
基于图形的统计显示

## Slide 77: 实时查看RDA Statistics
配置统计选项
不同Application对应的统计选项，请参阅附录。

## Slide 78: 实时查看RDA Statistics
基于列表的Fine Statistics

## Slide 79: 实时查看RDA Statistics
基于列表的Normal Statistics

## Slide 80: 保存统计日志
Save Current Detailed Results

## Slide 81: 保存统计日志
Save Historical Detailed Results

## Slide 82: 实时抓取PDU
RDA支持实时抓取任意Node/Application/Host的PDU.
为了在RDA客户端直接打开抓取的PDU日志，请先安装Wireshark并把Wireshark安装路径添加至系统环境变量。
  Wireshark下载路径： https://www.wireshark.org/download.html
  添加系统环境变量

## Slide 83: 实时抓取PDU
右键点击对应的Node/Application/Host，在弹出的菜单里选择Capture PDU’s.

## Slide 84: 实时抓取PDU
可以按照抓取包的数目，抓取的时间和包的长度来定义抓取时长。
可以限定抓特定源或目标IP地址的包，默认设置和当前选择的Application相关，如果去掉IP限定的话，将抓取所有的包，和当前Application无关。

## Slide 85: 实时抓取PDU
抓包的控制窗口在屏幕下方，可以随时停止抓包，也可以查看、保存或者删除抓取的文件。

## Slide 86: 支持和帮助
RDA基本信息

## Slide 87: RDA基本信息
请尽可能提供以下信息和日志以协助RDA问题定位
  Current/Historical Detailed Results
  RDA脚本
  System logs
  Chassis Information
  脚本正在运行时读取的Card Resource Usage
  cli.log

## Slide 88: RDA基本信息
System Logs/Chassis Info/Card Resource Usage

## Slide 89: RDA基本信息
通过FTP Client登录Edge（默认IP：192.168.10.200）
  用户名：cli
  密码：diversifEye
下载cli.log
cli.log

## Slide 90: Appendix
Gracefully Reboot and Restart RDA
RDA Management Web Interface
Normal/Fine Statistics
VLAN Configurations
Upgrade System and License Installation
Additional Applications Introduction
Troubleshooting

## Slide 91: Gracefully Restart and Shutdown RDA
via RDA Client GUI
via SSH

## Slide 92: Restart and Shutdown RDA
重启和关机RDA的两种方式
  RDA Client GUI
    对于Edge & Core的配置，通过此方式将同时重启或下电两台设备。
  SSH
    对于Edge & Core的配置，需要分别SSH到Edge（默认IP: 192.168.10.200）和Core（默认IP: 192.168.10.201）进行重启或下电的操作。
    重启
      用户名：reboot 密码：restartd
    关机
      用户名：poweroff 密码：shutdown
  注意：异常断电可能导致RDA损坏，需要返厂维修，所以请不要强行下电或拔电源。

## Slide 93: Restart and Shutdown RDA
via RDA Client GUI

## Slide 94: Restart and Shutdown RDA
via SSH

## Slide 95: RDA Management Web Interface
Download System Logs
diversifEye System Information
Card Resource Usage
Client Install
Online Help
Global Settings for All Cards
Admin – Network Properties
Admin – Global Settings for Each Cards

## Slide 96: Home – Admin
Download System Logs

## Slide 97: Home – Admin
Username/Password

## Slide 98: Home – Admin
diversifEye Chassis Information

## Slide 99: Home – Admin
Chassis Info - diversifEye System Information

## Slide 100: Home – Admin
Chassis Info - diversifEye License Information

## Slide 101: Home – Admin
Card Resource Usage

## Slide 102: Home – Admin
Card Resource Usage

## Slide 103: Home
Client Install

## Slide 104: Home
Online Help

## Slide 105: Home – Admin
Global Settings – All Cards

## Slide 106: Home
Admin

## Slide 107: Home – Admin
Network Properties

## Slide 108: Home – Admin
Global Settings

## Slide 109: Home – Admin
Global Settings - Select Cards

## Slide 110: Home – Admin
Global Settings – Host IPv6 Settings

## Slide 111: Home – Admin
Global Settings – Mandatory Configurations for IPv6

## Slide 112: Applications & Hosts Properties
Applications
  FTP/VoLTE/TeraFlow/RTSP/PING/HTTP/TWAMP
Hosts
  Gateway/Internal Server/External Server/PPPoE

## Slide 113: Applications – FTP
Overview

## Slide 114: Applications – FTP
Command Lists (get)

## Slide 115: Applications – FTP
Command Lists (put)

## Slide 116: Applications – FTP
Internal Server Resource List

## Slide 117: Applications – FTP
Shared Client Resource List

## Slide 118: Applications – FTP
FTP Client Properties

## Slide 119: Applications – FTP
TCP Characteristics Properties

## Slide 120: Applications – FTP
FTP Client Properties

## Slide 121: Applications – FTP
FTP Client Properties & Profile

## Slide 122: Applications – FTP
Add Profile

## Slide 123: Applications – FTP
Add Profile

## Slide 124: Applications – FTP
FTP Server Properties

## Slide 125: Applications – FTP
FTP Server Properties

## Slide 126: Applications – VoLTE
Overview

## Slide 127: Applications – VoLTE
Add Codec AVP

## Slide 128: Applications – VoLTE
Add Codec AVP

## Slide 129: Applications – VoLTE
VoIP UA Properties

## Slide 130: Applications – VoLTE
Authentication Details

## Slide 131: Applications – VoLTE
VoIP UA Properties

## Slide 132: Applications – VoLTE
VoIP UA Properties

## Slide 133: Applications – VoLTE
RTP Stream Profiles

## Slide 134: Applications – VoLTE
RTP Stream Profile Properties

## Slide 135: Applications – VoLTE
VoIP Call List Properties

## Slide 136: Applications – VoLTE
External VoIP Proxy Properties

## Slide 137: Applications – DL UDP
TeraFlow Client Properties

## Slide 138: Applications – DL UDP
TeraFlow Client Properties

## Slide 139: Applications – DL UDP
TeraFlow Server Properties

## Slide 140: Applications – DL UDP
TeraFlow Server Properties

## Slide 141: Applications – DL UDP
TeraFlow Server Properties

## Slide 142: Applications – UL UDP
TeraFlow Client Properties

## Slide 143: Applications – UL UDP
TeraFlow Client Properties

## Slide 144: Applications – UL UDP
TeraFlow Server Properties

## Slide 145: Applications – RTSP
RTSP Client Properties

## Slide 146: Applications – RTSP
RTSP Client Properties

## Slide 147: Applications – RTSP
RTSP Client Properties

## Slide 148: Applications – RTSP
RTSP Stream Profile Properties

## Slide 149: Applications – RTSP
RTSP Stream Profile Properties

## Slide 150: Applications – RTSP
RTSP Server Properties

## Slide 151: Applications – RTSP
RSTP Server Properties

## Slide 152: Applications – PING
Ping Application Properties

## Slide 153: Applications – PING
Ping Application Properties

## Slide 154: Applications – HTTP
HTTP Client Properties

## Slide 155: Applications – HTTP
HTTP Client Properties

## Slide 156: Applications – HTTP
HTTP Client Properties

## Slide 157: Applications – HTTP
HTTP Server Properties

## Slide 158: Applications – HTTP
HTTP Server Properties

## Slide 159: Applications – HTTP
Request Lists (GET)

## Slide 160: Applications – HTTP
Request Lists (POST)

## Slide 161: Applications – HTTP
Request Lists (POST)

## Slide 162: Applications – HTTP
Internal Server Resource List

## Slide 163: Applications – TWAMP
TWAMP Client Properties

## Slide 164: Applications – TWAMP
TWAMP Client Properties

## Slide 165: Applications – TWAMP
TWAMP Server Properties

## Slide 166: Hosts – Gateway

## Slide 167: Hosts – Internal Server
Host Properties

## Slide 168: Hosts – Internal Server
Host Properties

## Slide 169: Hosts – Internal Server
Host Properties

## Slide 170: Hosts – Internal Server
Host Properties

## Slide 171: Hosts – External Server
Host Properties

## Slide 172: Hosts – PPPoE
Host Properties

## Slide 173: Hosts – PPPoE
Host Properties

## Slide 174: Normal/Fine Statistics

## Slide 175: Applications – FTP Client

## Slide 176: Applications – FTP Server

## Slide 177: Applications – VoLTE

## Slide 178: Applications – RTSP Client/Server

## Slide 179: Applications – PING

## Slide 180: Applications – HTTP Client/Server

## Slide 181: Applications – TWAMP Client/Server

## Slide 182: Hosts – Internal Server/PPPoE

## Slide 183: VLAN Configurations

## Slide 184: VLAN Configurations
请参阅TTK780_001_Issue_3.pdf

## Slide 185: Upgrade System & License Installation

## Slide 186: RDA Upgrade System
RDA软件版本升级，请联系TM500 FAE.

## Slide 187: Additional Applications
Voice services
Video services
Media & Voice Passive Analysis
TWAMP – Two Way Active Measurement
Thresholding
TeraFlow
SMS over IMS

## Slide 188: Voice services
Will Voice be “just” data?
Explosive demand, increasing price pressure and OTT competition drive VoLTE
Opens new business opportunities
Helps improve customer experience
Cobham VoLTE option allows emulation of VoLTE UEs with different audio codecs to ensure that the coveted QoE improvements are achieved, VoLTE traffic is prioritized appropriately through the entire network and performance can be optimized
4G Americas VoLTE_RCS TECHNOLOGY ECO-SYSTEM AND EVOLUTION

## Slide 189: Video services
Video on demand (VoD) and video streaming (VS) are the most popular applications in LTE networks and thus are under most scrutiny for quality of experince.
Cobham Video service option allows emulation of UEs connecting to VoD or VS servers as well as emulation of these servers to see the impact on the network performance or to see the network impact on the Video service performance.
Cobham implementation supports multiple Audio and Video codecs which allows users to test with scenarios that reflect their own network or to evaluate planned deployment performance.
Ericsson-mobility-report-june-2014

## Slide 190: Media & Voice Passive Analysis
Service’s overall quality is how the video or the audio quality is perceived by consumers. This is typically examplified with Mean Opinion Score (MOS). Cobham’s Passive Analysis option allows to quantify how network layer imperfections affect this quality of experience (QoE) factor.
Cobham implementation supports both audio and video quality analysis and also uses:
Jitter Buffer models real UE packet queuing and playback effects to
  detect lost packet
  Predict which packets would be discarded
Markov Model to statistically learn the distribution of lost and discarded packets during a call, and then apply this distribution for MOS calculation

## Slide 191: TWAMP – Two Way Active Measurement
Measuring the performance of IP networks is a challenge
  Standard tools were designed for simple troubleshooting
The Two-Way Active Measurement Protocol (TWAMP)
  defines a flexible method for measuring round trip IP performance among any two devices in a network that support the standard
  provides a flexible choice of solutions and full visibility into network performance
Cobham TWAMP option is
Compliant to work with any network element that supports TWAMP
Allows measurements between any two endpoints
IP performance can be measured effectively at all locations in the network
Notes: Measuring the performance of IP networks through the use of standard protocols has always been a challenge.
  The inventors of IP provided some tools, such as ICMP Ping, Traceroute and UDP Echo, as part of the TCP/IP suite of protocols.
Measuring the performance of IP networks through the use of standard protocols has always been a challenge. These tools were not intended to conduct overall performance measurements but were designed for simple troubleshooting of IP networks.
The Two-Way Active Measurement Protocol (TWAMP) defines a flexible method for measuring round-trip IP performance among any two devices in a network that support the standard.
TWAMP provides a flexible choice of solutions and full visibility into network performance
It is compliant to work with the routers and switches in the network.
  Any two endpoints can interoperate and therefore obviate the need for managers to deploy systems with closed proprietary protocols for measuring performance.
  Standards-based performance measurement protocols to create an ecosystem where IP performance metrics are obtained through cooperation among network elements.
Through the use and deployment of TWAMP the IP performance can be measured effectively at all locations.

## Slide 192: Thresholding
Cobham Thresholding Option
automatically determines if the expected performance criteria has not been met during testing
Saves time by identifying what, where and when it has been outside of tolerance
Allows monitoring of multiple applications simultaneously with different criteria
  Different UE groups (for example VIP customers and data only subscriptions) can have individual criteria
  Setting up different violation and clearance duration

## Slide 193: TeraFlow
Cobham TeraFlow Option creates TCP and/or UDP protocol traffic. This allows easily create “background” traffic while validating that other applications maintain acceptable level of performance.
Cobham TeraFlow Option
Generation of traffic at pre-defined level
Mirroring the UE data back for bi-directional measurement
Can be configured and turned On and Off per UE

## Slide 194: SMS over IMS
The IP Multimedia System (IMS) is not only used for VoLTE, but also to deliver other services such as traditional messaging services (SMS).
Cobham SMS option allows emulation UEs to connect to IMS SMS servers and ensure that the coveted integration of SMS services function properly and transmission and reception of SMS messages works properly through the entire network.
Nielsen Mobile-Consumer-Report-2013

## Slide 195: Troubleshooting

## Slide 196: Troubleshooting
检查脚本Physical Interface是否和当前RDA硬件配置匹配。
  例如，当前RDA脚本是基于D500 Pairt （Core & Edge）Partition 1生成的，那么对应的Physical Interface分别为10/1/0（Host -> PPPoE）和20/1/1（Host -> Internal Server），如果导入Standalone D500，则需先用文本编辑器把Server对应的Physical Interface更新为10/1/1。
可以用文本编辑器批量替换修改RDA脚本。
  例如，把基于Partition 1生成的脚本导入Partition 2使用，则在导入脚本前，需要批量替换PPPoE对应的所有Physical Interface。
脚本无法导入RDA内

## Slide 197: Troubleshooting
检查网线连接是否正确，尤其是RDA Hub上的端口是否和当前分区对应。
  例如，如果当前使用单台D500，并且使用的是分区2，那么RDA的Gb2口应该连接到Hub的1口，TM500的PPPoE口连接到Hub的3口，核心网SGi口连接到Hub的6口。
另外，还需注意TM500侧连接的网口是否是正确的PPPoE口（在TM500上排HLP卡上）。
检查TM500 PPPoE IP地址是否配置正确，可以通过串口线连接到TM500上排的HLP卡查看配置，PPPoE地址为other(o)字段内I2=后面的IP地址。
PPPoE IP地址获取不到

## Slide 198: Troubleshooting
检查RDA脚本内PPPoE的IP地址是否与TM500 PPPoE口的IP地址一致。
PPPoE IP地址获取不到

## Slide 199: Troubleshooting
检查RDA脚本内PPPoE的Physical Interface是否正确。例如，如果当前使用单台D500，并且使用的是分区3，那么PPPoE的Physical Interface应该是12/1/0。
如果以上配置和连线都没有问题，那么需要检查VLAN配置是否正确。注意单台RDA和一对RDA使用时配置的不同。比如，单台D500时，只需要一个Hub，VLAN 10在2口，VLAN11在3口，VLAN12在4口为Untag状态，VLAN16在5口，VLAN17在6口，VLAN 18在7口为Untag状态；一对D500时，需要两个HUB，VLAN 10~15分别在EDGE HUB的2~7口上Untag，VLAN 16~21分别在CORE HUB的2~7口上Untag。
PPPoE IP地址获取不到

## Slide 200: Troubleshooting
检查TMA脚本内，RDA脚本名称和分区等信息是否配置正确。
TM500控制口和RDA管理口Gb1需连在同一个Hub，且它们的IP在同一个网段。
TMA无法调用RDA脚本

## Slide 201: Troubleshooting
请先检查FTP/HTTP/UDP Server能否Ping通Gateway和pppoe_0000_0.
  在RDA客户端Hosts页面，右键点击FTP/HTTP/UDP Server，选择Ping From；
如何调试RDA业务不通

## Slide 202: Troubleshooting
  选择Entity type为Host，然后点击IP address右边的小图标；
如何调试RDA业务不通

## Slide 203: Troubleshooting
  选择Host为Gateway；
如何调试RDA业务不通

## Slide 204: Troubleshooting
  确保从FTP/HTTP/UDP Server可以Ping通Gateway；
  同理，请确认从FTP/HTTP/UDP Server可以 Ping通pppoe_0000_0；
如果FTP/HTTP/UDP Server无法Ping通Gateway，请确认：
  Gateway是否可Ping；
  Gateway/FTP/HTTP/UDP Server IP及子网掩码是否配置正确；
如何调试RDA业务不通

## Slide 205: Troubleshooting
  尝试找一台电脑，把IP配置为Gateway的IP，然后连接到VLAN Hub对应的SGi口，确认能否从FTP/HTTP/UDP Server Ping通这个IP，以确定是Gateway还是Gateway与SGi连接网线引起的异常；
如果FTP/HTTP/UDP Server都能Ping通Gateway和pppoe_0000_0，但是Shenick依然业务不通，请检查FTP/HTTP/UDP Server属性所配置的MTU是否超过了EPC/eNB配置的MTU。
如何调试RDA业务不通

## Slide 206: Troubleshooting
比如VoIP测试中，有些问题会随机出现在某些UE上，如果问题出现之后再到对应的Application上抓取PDU，将不能抓到出问题时的log，如果提前抓取，又不确定问题会出现在哪些UE上。对于这种情况，可以随意选择一个UE的Application然后在抓取PDU时去掉对于源和目标IP地址的限制，这样就可以抓取所有UE的log了，问题出现之后，再在WiresharK内过滤出对应UE的IP地址就可以了。
无法抓取有效的出问题UE的PDU

## Slide 207: References
Real Data Apps Overview.pptx
RDA_D500-D1000.pptx
TTK780_001_Issue_3.pdf

## Slide 208: Change History
Version | Date | Author | Reviewed by | Approved by | Change history
0.1 | 10/05/2016 | Klein Jiang | NA | NA | Initial draft
0.2 | 29/05/2016 | Klein Jiang | NA | NA | Reviewed by Corey/Sining
0.3 | 21/06/2016 | Klein Jiang | NA | NA | Reviewed by Klein
0.4 | 25/07/2016 | Klein Jiang | NA | NA | Update