## Slide 1
TM500 Training for Customer X
Presented by: Alex Blackwood
Principal Field Application Engineer
July 2015

## Slide 2: D500 Traffic Generator / Analyser
Notes: 1/12/2016
Proprietary
1

## Slide 3: Confusion about the DiversifEye
You will see names like DiversifEye, D500, D1000, and Shenick
  DiversifEye is the actual product name for the device that is used to generate data traffic in the E500
  DiversifEye is the software that you use to interact with the D500
  Shenick is the name of our former partner company that produces the DiversifEye
  Shenick is now Aeroflex!! 
  Aeroflex is now Cobham!!  

## Slide 4: Flavors of DiversifEye
The DiversifEye comes in two hardware configurations. In one configuration there are two boxes and in the other there is one box
  In the two box configuration
    One box is a network Edge box; it connects to UEs
    One box is a network Core box; it connects to the ePC
    This configuration supports 6 simultaneous users
  In the one box configuration the Edge and the Core are in one box
    This configuration supports 3 simultaneous users

## Slide 5: What is the DiversifEye?
It is a Real Data Traffic Generator
What does it do?
  When integrated with the E500 it provides multiple data services running in parallel for thousands of UEs in a multi-cell environment
  Simulates applications such as HTTP, FTP, VoIP, VoLTE, Video
  Client & Server simulation
  Enables
    End to end network testing
    Quality of experience measurements
    Application level measurements per flow
    e.g. latency, jittering etc
  Supports 6 users:
    One TM500 per user, One shared DiversifEye
It can also be used with standalone EMUE or MUE

## Slide 6: DiversifEye in the System
EPC
DiversifEye Edge/Core
TM500
UL traffic gen
& DL analysis
DL traffic gen
& UL analysis

## Slide 7
PROPRIETARY & CONFIDENTIAL
6
Default Management IP Address
192.168.10.200 Edge Static IP
Connect via Standard Web Browser
Notes: Add real people testing

## Slide 8
PROPRIETARY & CONFIDENTIAL
7
In a standard Web Browser type D500 Edge IP Address
Click on “Download diversifEye X.y Client”
Installers Provided: -
  Windows (XP and 7)
  MAC OSX (Snow Leopard and Lion)
  Linux (Fedora/Centos/Redhat and UBUNTU)
  Solaris
Download GUI Client
Notes: Add real people testing

## Slide 9
PROPRIETARY & CONFIDENTIAL
8
Install GUI Client
For Installation Instructions client “Client Install” on Web Admin view
After Installing GUI Client load the GUI Client login dialogue
  Username: ‘tm500’
  Server Host: 192.168.10.200
  Partition: 1
Notes: Add real people testing

## Slide 10
PROPRIETARY & CONFIDENTIAL
9
Java GUI Client View
  Click on ‘Nodes’ tab to check Status of Test Agent Cards
Notes: Add real people testing

## Slide 11
PROPRIETARY & CONFIDENTIAL
10
D500 Edge Standalone – Test Agent View
Notes: Add real people testing

## Slide 12
PROPRIETARY & CONFIDENTIAL
11
Flow Processor | VLAN Tag | Partition (User)
10/0 | 10 | 1
11/0 | 11 | 2
12/0 | 12 | 3
10/1 | 16 | 1
11/1 | 17 | 2
12/1 | 18 | 3
Accommodates 1-3 Users
Client or Server Emulation
Physical Ports
  GB1: Management Interface
  GB2: Test Traffic Port
D500 Standalone Interface Specifications
Notes: Add real people testing

## Slide 13
PROPRIETARY & CONFIDENTIAL
12
User1
  P1 10/0 tm500
User2
  P2 11/0 tm500
Flow Processor | VLAN Tag | Partition (User)
10/1 | 16 | 1
11/1 | 17 | 2
12/1 | 18 | 3
username
D500 Edge Logical Test Port/Partitions
Notes: Add real people testing

## Slide 14
PROPRIETARY & CONFIDENTIAL
13
D500 Edge Standalone Logical Connectivity
Typical Logical Port Assignment for Edge Standalone
  1 GUI Client per D500 partition – controlling 2 different VLANs
Notes: Add real people testing

## Slide 15
PROPRIETARY & CONFIDENTIAL
14
D500 Edge Standalone in Ex-MUE Solution
Typical Benchtop Setup
Notes: Add real people testing

## Slide 16: HP Switch VLAN configuration
Each D500 is internally divided with 6 partitions with different VLAN tagging. We can access different partitions using different VLAN tag from a single data port.
VLAN tags from10-12 is for Edge and 16-18 is for Core.
M
18
17
16
12
11
10
1
Management
Data

## Slide 17: DiversifEye Control
The DiversifEye can be controlled in multiple ways
  Via the DiversifEye GUI software
  Via a Command Line Interface (CLI)
  Via E500 embedded software running in MTS/ NAS mode
The most convenient method is to use the DiversifEye with EMUE or E500 running in MTS/NAS mode
The CLI can be used for automated control, especially when using MUE
The EMUE/E500 embedded software actually uses the CLI to control the DiversifEye when running in MTS/NAS mode

## Slide 18: DiversifEye DiversifEye GUI Control
Controling the DiversifEye via the DiversifEye GUI
  The DiversifEye GUI is a Java based GUI

## Slide 19: DiversifEye CLI Control
The CLI interface is a Telnet or SSH based interface.
  Username is “cli”, password is “diversifEye”
The CLI is best used in an automation script
  The user can load/list/select/start/stop test groups
  Get statistics , display threshold events
From the command line you can get help
  To see all available commands and description log in and give the command cli help

## Slide 20: DiversifEye Usage
There are two steps to using the DiversifEye
  Step 1: Provisioning
    Sets up test cases for use later
    Builds XML files that are used by the DiversifEye during normal operation
  Step 2: Data Traffic Generation
    Uses the provisioned XML files to generate data traffic for UEs
    Controlled via the CLI by either
      The Diversify GUI
      The EMUE/E500 embedded software
      Automation scripts

## Slide 21: DiversifEye Provisioning
Each EMUE/E500 release comes with templates and scripts to help provision the DiversifEye.
  These files are installed into the Program Files directory
  Aeroflex/TM500/<Release>/diversifEye
There are two files that will need editing
  live.bat
  TM500.xml

## Slide 22: DiversifEye Provisioning – Live.bat
Live.bat is a windows batch file that helps automate the provisioning. It sets up some variables, then calls a Python script Shenick.py.
Modify the following in Live.bat as needed
  set aflx_ip_addr=192.168.10.200
  set aflx_group_name=TM500LteTestPfc
  set aflx_part=1

## Slide 23: DiversifEye Provisioning – TM500.xml
TM500.xml is the file that you modify to create your test cases
This file has the following primary blocks in it

## Slide 24: DiversifEye Provisioning – TM500 Block
TM500 block includes below parameters.
  Total_UEs : No of UEs need to be configured in the script
  Minimum_UE_ID_Digits : This is the no of digits need to represent UE id in “Host name” or “application name” in test group. It should be same as in command DECONFIGRDASTARTTESTCASE.
  PDNs_per_UE : No of PDN we need to configure per UE
  LAN_IP : This is the IP address of AC DTE port usually Tsec1

## Slide 25: DiversifEye Provisioning – PPPoE Block
PPPoE block includes below parameters
  MAC_Start : arbitrary start MAC address for all PPPoE hosts
  diversifEye_Port : 0 is for client and 1 is for server. As we are setting up PPPoE for client the default value is 0.
  MTU : Here we can define MTU size.

## Slide 26: Application Configuration Block
Application_Configuration block includes below parameters.
  Server Application : In this block we can set different parameters required for setting up, FTP server, Web server (HTTP server), SIP Server and RTSP server. There are different server blocks for each server.
  Client Profiles : Here we have to configure client application (FTP, HTTP client etc ) configuration details. All the client application are defined inside the client profiles block.

## Slide 27: DiversifEye Provisioning – Client Configuration
Further client application has two parts. One is default configuration and 0-n profiles configuration.
  Default : This is the default application configuration which is associated with a particular client Host. There is one to one mapping between each default application and a host.
  Profile_n : There can be multiple additional applications can be associated with a particular Host profile configuration.
NOTE: There can be one default and multiple profiles associated with one Host.

## Slide 28: DiversifEye Provisioning – FTP Configuration
Server Configuration
Client configuration

## Slide 29: DiversifEye Provisioning – HTTP Configuration
Server Configuration
Client configuration

## Slide 30: DiversifEye Provisioning – VOIP Configuration
Server Configuration

## Slide 31: DiversifEye Provisioning – VOIP Configuration
Client Configuration

## Slide 32: DiversifEye Provisioning – RTSP Configuration
Server Configuration
Client configuration

## Slide 33: DiversifEye Edge Usage
The DiversifEye Edge Connects to the Access Concentrator
Each Virtual UE in the system creates PPPoE sessions for each assigned IP address and/or PDN
DiversifEye Edge Clients create PPPoE sessions with the Virtual UEs
The E500 embedded software then starts and stops data sessions based scripts

## Slide 34: DiversifEye Core Usage
The DiversifEye Core Connects to the RAN SGi Interface
The DiversifEye Edge controls creation of servers on the DiversifEye Core
The E500 embedded software then starts and stops data sessions based scripts

## Slide 35: Scripting with the Ext-MUE gui
RDA applications can also be controlled via TMA scripting. Useful when unmanned automation is needed. It also simplifies the need to control diversifEye separately.
Operating Data Applications with RDA
Three main commands, normally used in the following order:
Start RDA Test Case – Configures the partition used, Test group, IP address etc…
Set RDA Service State – Configures the service state for applications such as ftp_put, ftp_get, UDP uplink / downlink etc…
Stop RDA Test Case – Stop all the applications and services for the partition used.

## Slide 36: Scripting
Example use of Start RDA Test Case
Operating Data Applications with RDA
Note: Start RDA Test Case will stop any existing diversifEye test group before starting current test group

## Slide 37: Scripting
Example use of Set RDA Service State
Operating Data Applications with RDA